## Slide 1
HEAT EXCHANGER FOULING PREDICTION USING MACHINE LEARNING
MACHINE LEARNING FOR CHEMICAL ENGINEERING PROJECT
Sarthak Srivastava - 2022A1PS0889G
Khusboo Jain - 2022A1PS1450G
Shaachi Khanna - 2022A1PS1477G
Balram Bhala - 2023A1PS0116G
CHE F315

## Slide 2
PROBLEM STATEMENT AND MOTIVATION
Heat exchanger fouling is one of the major operational issues in petroleum and chemical processing industries. With increasing run-time, tubes accumulate deposits, reducing heat transfer efficiency and increasing energy consumption.
Objective:
To develop machine learning models that can predict Heat Exchanger Performance Ratio (HEPR) using crude properties, process operating conditions, and engineered thermal features.
Why ML?
  Process fouling is highly nonlinear
  Difficult to predict analytically
  ML enables early detection and schedule
  optimization
  Helps avoid shutdowns & improves refinery energy efficiency

## Slide 3
DATA SET DESCRIPTION
Dataset:
Industrial dataset containing E-03 preheat train exchanger operating data:
  ~64,000 rows (Downsampled to every 10 hours)
  Crude properties (API, TAN, Chlorides)
  Crude & diesel temperature profiles
  Mass flow rates
  Heat capacities
  Operating hours
Target Output:
HEPR = Actual Heat Duty / Design Heat Duty
Final Dataset → 14 input features + 1 output

## Slide 4
Input Features (X):
  Crude API gravity
  Crude TAN
  Crude chlorides
  Tube-side temperatures (in/out)
  Mass flow rate
  Cp
  Shell-side temperatures
  Shell-side mass flow rate
  ΔT (engineered)
  Shell ΔT (engineered)
  Operating time (hr and days)
Output Feature (y):
  HEPR (Heat Exchanger Performance Ratio)
HEPR < 1 → fouling happens
HEPR ≈ 1 → ideal clean conditions
INPUT FEATURES & OUTPUT VARIABLE

## Slide 5
ML MODELS
ML Model Used - Regression
  Multiple Linear Regression (MLR)
  Support Vector Regression (SVR – RBF kernel)
  Principal Component Regression (PCR)
Reason for Selection:
  Regression is suitable since HEPR is a continuous variable
  MLR → baseline model
  SVR → good for nonlinear relationships
  PCA/PCR → dimensionality reduction & multicollinearity handling

## Slide 6
EDA - HISTOGRAMS OF INPUT FEATURES

## Slide 7
EDA - KDE PLOTS

## Slide 8
EDA - KDE PLOTS

## Slide 9
BOX PLOTS

## Slide 10
BOX PLOTS

## Slide 11
SCATTER PLOTS

## Slide 12
SCATTER PLOTS

## Slide 13
CORRELATION HEATMAP

## Slide 14
PAIR
PLOTS

## Slide 15
MLR - INTERCEPT & COEFFECIENTS

## Slide 16
MLR - PERFORMANCE METRICS

## Slide 17
MLR - PARITY PLOTS

## Slide 18
MLR - 5 FOLD CROSS VALIDATION

## Slide 19
SVR - PERFORMANCE METRICS

## Slide 20
SVR - PARITY PLOTS

## Slide 21
SVR - 5 FOLD CROSS VALIDATION

## Slide 22
PCA

## Slide 23
PCA

## Slide 24
PCR - PERFORMANCE METRICS

## Slide 25
PCR - PARITY PLOTS

## Slide 26
PCR - 5 FOLD CROSS VALIDATION

## Slide 27
CONCLUSION
Among the three models (MLR, SVR, PCR), the Support Vector Regression (SVR) model provides the most reliable and realistic performance.
SVR achieved a Test R² of 0.9825 with an RMSE of 0.0055, indicating excellent predictive accuracy and strong generalization.
While MLR shows extremely high R² values (~0.999), this is largely due to strong linear dependencies introduced by engineered features and does not fully capture the nonlinear fouling behavior.
PCR performs well (Test R² = 0.955), but SVR outperforms both models and is therefore identified as the best model for predicting heat exchanger fouling (HEPR).

## Slide 28
THANK YOU